Section 325	Construction Grade Driveways

Any Zoning Permit issued for a new principle use structure, in which case said use shall require the installation of a new driveway intersecting and abutting any public thoroughfare, and where said new driveway shall be the access to and from the site of the new structure by  construction and site preparation vehicles (well-drillers, dump trucks, lumber deliveries, etc); and/or any new timbering, lumbering, clearing or other site-preparation activity, shall also require that a (Construction Grade Driveway( be installed prior to any other activity regarding the site in preparation for construction/activity.

A (Construction Grade Driveway( shall meet the following requirements:

1	Materials required for use in (construction-grade driveway(.

The (construction grade driveway( shall consist of AASHTO#1 or R-3 placed 8" thick over geotextile fabric at a width of 20' minimum for a distance of 50' minimum from the edge of the road.  Additional stone (2A aggregate) shall be placed immediately adjacent to the road pavement as required to protect the shoulder from damage.

2	Weight-bearing standards of (construction-grade driveway(.

The (construction grade driveway( shall be of suitable thickness to carry the weight of a fully loaded tri-axle dump truck.  The contractor shall be required to place additional stone as required to provide a stable base for all vehicular traffic.

3	Maintenance and upkeep of (construction-grade driveway(.

The thickness of stone shall be constantly maintained to the specified dimensions by adding additional stone.  A stockpile shall be maintained on site for this purpose.

4	The (construction-grade driveway( shall be maintained and kept to standards (see above) in order to protect the integrity of the shoulder of the road, and the construction of the cartway, and to be abutted to the cartway so that damage shall not occur due to heavy vehicles and/or machinery causing collapse of the paved surface of the cartway.

5	Further, it shall be the responsibility of the Zoning Permitee, or his/her designee (contractor), to assure that no construction materials or debris, earth (dirt), stones, or any other extraneous material is deposited or abandoned on the cartpath of the public thoroughfare accessed.  Upon notification by the Zoning Officer of the need to remove the material/debris by close of the business day (5:00 PM), and failure of the responsible party to comply with said requirement; the Zoning Officer shall cite the responsible party, notifying them that such material/debris has been deposited on the cartpath and not properly removed, and further that the Zoning Officer shall issue a (Stop Work( order to remain in place until the citation is complied with.  If compliance has not occurred within twenty four (24) hours of the citation, the Zoning Officer shall be authorized to institute civil enforcement proceedings as a means of enforcement.  Any responsible party who violates this provision shall be liable as described in Section 700.4 of this Ordinance.

Reprinted from Monaghan Township Zoning Ordinance, adopted May 14, 2007